## Slide 1: FCC Meeting
CBRS License Areas and Practical Deployment of Network CBSDs
April 3, 2018

## Slide 2: CBRS Rules Create Substantial Deployment Problems
The CBRS rules currently specify the use of Census Tracts for Priority Access Licensees (PALs), which are very small license areas
AT&T requested CommScope to analyze the practical impact of the CBRS interference protection rules given the small market areas, based on part 96 rules
The study demonstrates that the small license areas will create significant deployment issues
  Unable to deploy so as to cover the entire tract
  Can deploy, but to cover the border areas, must severely limit power and deploy many more CBSDs than what may be actually needed
AT&T accordingly recommends substantially increasing the size of licenses in urban areas to limit near-border impacts

## Slide 3: Current CBRS Border Coordination Requirements
The rules specify a PAL protected area (PPA) based on a -96 dBm/10 MHz contour (47 CFR §96.26(c)(2))
  The PPA contour at maximum power in many cases, especially in urban areas, would be larger than the Census Tract and therefore the power would have to be limited to bring the PPA within the Census Tract boundary (47 CFR §96.26(c)(3)) or the PPA would be defined by the Census Tract boundary
The rules also provide for an aggregate CBSD signal level of -80 dBm/10 MHz for all CBSDs deployed around a Census Tract (47 CFR §96.41(d))
  The aggregate interference may impose limits that mean a provider may not be able to take advantage of the 47 dBm/10 MHz EIRP for outdoor devices in the band
  The -80 dBm/10 MHz limit creates a daisy-chain of relationships between adjacent tracts, and tracts adjacent to those tracts, etc
  To determine what impact a CBSD might have on a particular PAL in an adjacent Census Tract, you need to look at least two Census Tracts deep
The rules provides for outdoor CAT B power levels – 47 dBm/10 MHz
  CBRS use cases depend upon CAT B deployments

## Slide 4: The Model
AT&T chose the Census Tract that contains the FCC headquarters for illustrative purposes
  Average size of Census Tract is ~0.6-0.8 sq km
Impact of CBSD grant power in Census Tract A in protecting all other surrounding PAL licenses
  Directional antenna assumed in Census Tract A pointing 18˚ from North
No other protection entity considered except PPA
  Isolate impact of PPA to PPA protection
  FSS/GWBL presence may further constrict Tx power
CBSD parameters
Antenna beam width: directional 120˚/65˚.Can be considered three sectors
Antenna height: 15m
Max EIRP: 47 dBm/10 MHz
Antenna gain: 10 dB
Requested Tx EIRP: 37 dBm/MHz
CBSD category: B
Transmit frequency : 3645-3655 MHz
Notes: Can we get coloring of NPS tract consistent in red?

## Slide 5: Protection points for CBSD A in census Tract A
Recommended power of CBSD A will depend on protecting the PPA coverage areas on Census Tract P
  CBSD A orientation 18˚ from North
Restraining Protection points in Census Tract P are interfered aggregately by
  CBSD A in Tract A
  All CBSDs in Tract 1 through Tract 12
Census Tract license size forces the networks design to deploy many more CBSDs
Licensees cannot combine adjoining Census Tracts to simplify the network design
  There is no guarantee the that same channel would be granted to all the Census Tracts belonging to a licensee

## Slide 6: Engineering for Coverage
Commscope created an highly optimized network design
  Due to irregular shape of Census tract P, 5 CBSDs (17 to 21) with antennas pointing at various angles and beamwidths was required to provide coverage
  Figure shows -96 dBm/10 MHz contours based on 47 dBm/10 MHz EIRP at the locations shown
  The PPA is always truncated back to the Census Tract boundary
  47dBm/10 MHz power is based equipment capability and not necessarily the actual power grant allocated to the CBSD by the SAS
CBSD ID | EIRP Capability (dBm/10MHz | Azimuth Angle | Beamwidth
17 | 47 | 305 | 120
18 | 47 | 135 | 65
19 | 47 | 90 | 60
20 | 47 | 160 | 60
21 | 40 | 90 | 65
Category B
Antenna Height – 15m

## Slide 7: Interference Outside Census Tract
WinnForum bases protection area morphology on the average Land Use/Land Cover, so Census Tract P is “rural”
Using ITM propagation model for rural areas, a CBSD at 47 dBm/10 MHz would produce the signal levels shown:

## Slide 8: After Applying Interference Protection Limits
Applying IAP significantly limits power
  CBSD 12 need to be turned off to protect the PPA above Census Tract A using WinnForum “rural” propagation model
  Using “urban” model, CBSD 12 can transmit at 30 dBm/MHz, with sectorization to 65˚ improving the power by 1 dB to 31 dBm/MHz
PPA contour (-96 dBm/10 MHz) can be larger than the Census Tract in urban areas
  PPA contour most likely will be clipped by Census Tract
  Observed even with a single CBSD in the center
Census Tract boundary can significantly limit power to protect adjacent PAL
  To the extent in some cases inoperable, i.e. below EUD power @ 23 dbm/10 MHz
  Shape of the Census Tract can significantly reduce allocated power with substantial impact on viability of creating economic outdoor networks
  If CBSD 12 is placed at higher heights, further power reduction will be necessary

## Slide 9: Practical Impact on PAL Licensees
Unable to deploy so as to cover the entire Census Tract, or
Can deploy, but to cover the border areas, must severely limit power and deploy many more CBSDs than what may be actually needed.
  Increase in equipment costs
  Increase in maintenance costs
  More backhaul needed (more equipment and costs)
  More approvals for mounting CBSDs needed (local zoning, building owners, etc)

## Slide 10: PEAs as Alternative
Washington, D.C. PEA market boundaries shown
  District of Columbia Census Tracts shown in light blue
  ~50 km from DC center to nearest boundary
  Objective of PEAs is to put population center in middle—means border is typically less populated areas
For modeling, DC PEA is Urban/Suburban
  E-HATA model used

## Slide 11: Path Loss Models

## Slide 12: PPA Protection for DC PEA
Approximately 143 dB Path loss is realized at PPA contour
  EIRP 47dBm/10MHz and coverage contour is -96 dBm/10MHz
Approximately 127 dB path loss required to be below -80dBm/10MHz interference protection to adjacent Census Tract
  With 10 surrounding CBSD Path loss would be 137 dB
In urban and suburban environment
  At least 2 km distance needed to realize ~127-137 dB loss
  Protection with mean (not median) -80 dBm/10MHz with the current WinnForum requirement will add 10 dB more
  Will require at least 4 km distance from transmitter to have interference below ‑80dBm/10MHz
PPA needs to be at least 2-4 km from transmitter site
  Significant Census Tract boundaries in DC are less than 0.5 km from centroid
PEA area allows to plan CBSD locations inward so that CBSD power is not interference limited by adjacent licensee
  Impossible to do this in Census Tract as it interferes with adjacent Census Tract even when placed in middle

## Slide 13: Conclusion
In urban areas, the small size of the Census Tracts can create significant practical deployment issues given the need to adjust power to protect adjacent licensees
Net impact is that providers will not be able to deploy networks operating at 47 dBm/10 MHz, but will instead be forced to very, very dense network deployments
  Super small cell deployments forced by protection of adjacent licensees
  Super small cell deployments forced by irregular borders of Census Tracts
Practical example using FCC Census Tract demonstrates 7 dB in power reduction
  FCC Census Tract is large compared to other Census Tracts bounding National Mall
  National Mall and Federal Triangle are precisely the types of areas where robust outdoor coverage would be beneficial
  Max allowed power from outdoor sites is essential to provide adequate indoor coverage
PEAs would permit deploying at max power for coverage and limiting impact of border areas