## Slide 1: Toyota Information to FCC Office of Engineering Technology
July 19, 2018

## Slide 2: State DOTs are Enthusiastic
61
127
317
259
69
179
210
75
Total Deployed & Planned = 3,530
11
26
6
20
1,500
26
30
20
3
252
27
30
12
16
118
75
DSRC V2I Roadside Units: Operational and Planned
26 States covering 79% of US population
10
51
Notes: The good news is that 25 states have committed to deploying 3,423 DSRC road side units.

## Slide 3: SAE Standard J2945: DSRC Channel Usage Plan
Reserved 5MHz
CH 172
Service
(safety only)
CH 174
Safety &
Service
CH 176
Safety &
Service
CH 178 Control
CH 180
Safety &
Service
CH 182
Safety &
Service
CH 184 Service
(safety only)
5.850 GHz
5.925 GHz
BSM = Basic Safety Message VRU = Vulnerable Road User PSM = Personal Safety Message C-ACC = Cooperative Adaptive Cruise Control SCMS: Security Confidential Management System
Every channel used for safety apps
Interleaved V2V and V2I limits interference
Seven 10-MHz Channels
US DSRC Spectrum
Ch. 172 | FCC restriction for safety: BSM safety and small set of I→V safety apps
Ch. 174 | I→V safety and mobility, to avoid cross-channel interference to Ch. 172
Ch. 176 | VRU safety (PSM) Person→V, and download from SCMS (I→V)
Ch. 178 | Control channel: Service availability announcement, Short safety services (I→V)
Ch. 180 | Non-BSM V2V safety (e.g. C-ACC, sensor sharing), and mobility (I→V)
Ch. 182 | I→V safety and mobility
Ch. 184 | FCC restriction for public safety. Ex: Preemption, Emergency Alert
Service availability announcement is via “WAVE Service Advertisement” (WSA), which announces a service that is assigned to a channel based on local factors (time and place). Examples: Curve Speed Warning, Merge Assistance Service, Weather Safety Information, SCMS Connection Availability. The term “advertisement” does not indicate that the service is a commercial service.
Notes: The answer is that the community had a master design for those applications.
They are seven channels, one for control and 6 for safety and service. This plan leaves safety application on every channel so that competition among them can be minimized. On top of that, it interleave the I2V and V2V transmissions. That helps reduction of cross-channel interference, further improving the communication performance. On another thing, there are many non-BSM applications. In other words, DSRC is much greater than BSM.

## Slide 4: 5GAA Test Results: First Problem - 2 Apples to 1 Apple
Every LTE V2X packet is sent TWICE
Every DSRC packet is sent ONCE
NOT APPLES TO APPLES

## Slide 5: 5GAA Test Results: Second Problem-DSRC is better than shown
X
Actual DSRC Performance:
= data from CAMP VSC-A test with Truck obstruction
See CAMP VSC-A Final Report
[CAMP configuration is 3 Mbps & 20 dBm; distances shown here are reduced by 2 dB from CAMP test data to match 5GAA configuration of 6 Mbps & 21 dBm]
5GAA DSRC results
inconsistent with DSRC field test data
X
X
VSC-A project:
+
X
Conclusion: DSRC meets all known application performance requirements